## Slide 1
IT4030 · INTERNET OF THINGS · PROJECT PROPOSAL
GreenPulse
A HEALTHIER HOME, A HAPPIER PLANT
Smart Agentic IoT Plant-Care Device with LLM Backend
Sensors
ESP32
Cloud
AI
Dashboard
PRESENTED BY
Kumarathunga R C S
IT23257054
Wathsala K L K
IT23182882
Senanayake Y M
IT23284470
Methsuka S A I
IT23160484
Lecturer: Mr. Uditha Dharmakeerthi SLIIT · Faculty of Computing · 2026
Notes: PRESENTER: Member 1 | TARGET: 20–25 sec | Running total ≈ 0:25 SCRIPT: "Good morning / good afternoon. We are presenting GreenPulse — A Healthier Home, A Happier Plant — our proposed smart agentic IoT plant-care system. GreenPulse combines real-time environmental sensing, secure IoT communication, cloud processing and LLM-based intelligence to transform raw plant-environment data into meaningful plant-care information." DELIVERY: Pause briefly on the title. Do not read out every team name; the slide shows them.

## Slide 2
02 · PROBLEM & MOTIVATION
Plants Need More Than Fixed Care Schedules
Manual Observation
Fixed Care Routine
Environmental Changes Missed
Poor Decision Support
01
Limited Monitoring
Traditional care relies heavily on manual observation — changes between inspections go unnoticed.
02
Raw Data ≠ Understanding
Sensor values alone may not tell users which care action is appropriate.
03
Missing Context
Local sensing alone cannot consider broader information such as the current weather.
How can raw environmental data become meaningful plant-care intelligence?
GreenPulse · IT4030 Internet of Things · Project Proposal
02
Notes: PRESENTER: Member 1 | TARGET: 50 sec | Running total ≈ 1:15 SCRIPT: "Traditional plant care usually follows the chain at the top of this slide: manual observation, a fixed care routine, environmental changes that get missed between inspections, and ultimately poor decision support. We see three core problems. First, limited monitoring — care relies on manual observation, so unfavourable conditions can go unnoticed. Second, raw data is not understanding — even when sensors exist, a soil-moisture or temperature value alone does not tell the user what action is appropriate. Third, missing context — local sensing alone cannot consider broader information such as the current weather. So the central question for our project is: how can raw environmental data become meaningful plant-care intelligence?" SOURCE: Proposal §1.1 Background and §1.2 Problem Statement.

## Slide 3
03 · PROPOSED SOLUTION
GreenPulse: From Sensing to Understanding
Plant
Environment
Sensors
Soil · DHT22 · BH1750
ESP32
Acquire · display
Secure MQTT
TLS · AWS IoT Core
Cloud + LLM
Store · understand
Node-RED
Visualize
User
Better decisions
MONITOR
Real-time plant environmental sensing on an ESP32 device.
Soil moisture · temperature · humidity · light
CONNECT
Secure, bidirectional MQTT communication with the cloud.
MQTT over TLS · AWS IoT Core · JSON
UNDERSTAND
Cloud and LLM-based contextual processing of the data.
Python · DynamoDB · LLM · weather · email
VISUALIZE
Real-time Node-RED monitoring and intelligent information.
Sensors · MQTT info · LLM input / output
GreenPulse · IT4030 Internet of Things · Project Proposal
03
Notes: PRESENTER: Member 1 | TARGET: 55 sec | Running total ≈ 2:10 SCRIPT: "GreenPulse answers that question with an end-to-end ecosystem. Environmental conditions around the plant are captured by sensors, processed on an ESP32, sent through secure MQTT to the cloud, interpreted with an LLM, and presented to the user on a Node-RED dashboard. We summarise the system in four capabilities: MONITOR — real-time sensing of soil moisture, temperature, humidity and light. CONNECT — secure, bidirectional MQTT communication over TLS. UNDERSTAND — cloud and LLM-based processing that adds weather and notification context. VISUALIZE — a Node-RED dashboard showing live data and the generated information. These four capabilities summarise the nine specific objectives in our proposal. Member 2 will now show how they fit into the overall architecture." HANDOVER → Member 2 (architecture). NOTE: If asked, the 9 objectives are in Proposal §1.5 (device, OLED/RGB, secure MQTT, cloud backend, LLM, weather + email, Node-RED, advanced features, evaluation).

## Slide 4
04 · OVERALL SYSTEM ARCHITECTURE
Four Layers, One Connected System
1
IoT Device
Sensing + device processing
Soil · DHT22 · BH1750
ESP32
OLED + RGB LED
Local status only
2
Secure Communication
Transport between device & cloud
Wi-Fi
MQTT over TLS · 8883
AWS IoT Core
Certificates · policies
3
Cloud Intelligence
Store, enrich & interpret
Python Backend
DynamoDB
Weather API
Email / Notifications
LLM
4
Visualization
Unified user interface
Node-RED Dashboard
User
Sensors · MQTT info · LLM I/O
GreenPulse · IT4030 Internet of Things · Project Proposal
04
Notes: PRESENTER: Member 2 | TARGET: 65 sec | Running total ≈ 3:15 SCRIPT: "GreenPulse follows a layered architecture that separates sensing, communication, intelligence and visualization. Layer 1, the IoT device: the soil-moisture, DHT22 and BH1750 sensors feed the ESP32, which drives the local OLED display and RGB LED. This layer provides local status only. Layer 2, secure communication: the ESP32 connects over Wi-Fi and uses MQTT over TLS on port 8883 to reach AWS IoT Core, our proposed MQTT broker, using certificate-based authentication and IoT policies. Layer 3, cloud intelligence: a Python backend receives the data, stores it in DynamoDB, retrieves weather and authorized notification information, and uses an LLM to generate contextual information. Layer 4, visualization: results are published back through MQTT to the Node-RED dashboard for the user. Importantly, communication is bidirectional — the device publishes telemetry and can also subscribe to cloud-generated topics." DELIVERY TIP: Walk top-to-bottom, pointing to each band. If you add animation in PowerPoint, reveal one band per click (Animations → Appear / Fade, "On Click"). NEXT: Member 1 returns for the hardware details on the next slide (see handover plan).

## Slide 5
05 · IOT HARDWARE & EMBEDDED SENSING
The ESP32 at the Heart of the Device
SENSING INPUTS
LOCAL OUTPUTS
Soil Moisture
Analog · GPIO34 · dry/wet calibration
DHT22
Digital · GPIO4 · temp & humidity
BH1750
I²C · GPIO21/22 · light in lux
ESP32
Acquire · validate · prioritise · publish
SOIL 45 %
TEMP 28.1 °C
HUM 62 %
LIGHT 320 lx
MQTT CONNECTED
OLED · readings + MQTT status only
Normal
Warning
Critical
Priority Critical > Warning > Normal
Separation by design: the device shows measurements and connectivity; AI-generated tips, quotes and summaries stay in the cloud and dashboard layer.
Display values are illustrative. Final thresholds will be set through calibration and prototype testing.
GreenPulse · IT4030 Internet of Things · Project Proposal
05
Notes: PRESENTERS: Member 1 (inputs) → Member 2 (ESP32 + outputs) | TARGET: 55 sec | Running total ≈ 4:10 MEMBER 1 (≈25 sec) — left column: "The device is built around the ESP32, chosen for its integrated Wi-Fi, GPIO, analog input and support for digital sensor interfaces. We propose three sensors: a soil-moisture sensor on analog GPIO34, which we plan to calibrate using dry and wet reference conditions; a DHT22 on GPIO4 for temperature and humidity; and a BH1750 on the I²C bus for light intensity in lux." HANDOVER (Member 1 → Member 2): "With the sensing hardware established, the next stage is converting these measurements into structured data and communicating them securely. Member 2 will explain the firmware and MQTT layer." MEMBER 2 (≈30 sec) — ESP32 + right column: "The firmware will acquire and validate readings, update the OLED, and evaluate priority for the RGB LED. The OLED shows only live readings and MQTT connection status. The RGB LED shows green for normal, yellow for warning and red for critical, with critical overriding warning, and warning overriding normal. By design, AI-generated tips, quotes and summaries are not shown on the OLED — they stay in the cloud and dashboard layer." FACTS: BH1750 + OLED share I²C (SDA GPIO21 / SCL GPIO22) if addresses are compatible. RGB on GPIO25/26/27 via current-limiting resistors. Final thresholds are set during calibration and prototype testing. Display values are illustrative.

## Slide 6
06 · SECURE MQTT & CLOUD ARCHITECTURE
Secure, Bidirectional Data Pipeline
ESP32
Publishes JSON
MQTT over TLS
Port 8883
AWS IoT Core
MQTT broker
Python Backend
Subscribe · validate
DynamoDB · LLM
+ external services
Node-RED
Subscribes · displays
Member 2 · device → broker
Member 3 · cloud processing
MQTT
Lightweight publish / subscribe via a central broker
Bidirectional: device ⇄ cloud
Topic-based message separation
QoS 1 for telemetry and AI responses
Security
MQTT over TLS (port 8883)
Device certificate + private key authentication
Least-privilege AWS IoT policies
No credentials in the public repository
Topic Structure
DEVICE → CLOUD
greenpulse/sensors
greenpulse/status
CLOUD → DEVICE + NODE-RED
greenpulse/ai/care
greenpulse/ai/weather
greenpulse/ai/notifications
GreenPulse · IT4030 Internet of Things · Project Proposal
06
Notes: PRESENTERS: Member 2 (MQTT + security) → Member 3 (cloud) | TARGET: 65 sec | Running total ≈ 5:15 MEMBER 2 (≈35 sec): "Here is the full data pipeline. The ESP32 formats readings as JSON and publishes them using MQTT — a lightweight publish/subscribe protocol where devices exchange messages through a central broker. It supports bidirectional communication and topic-based separation, and we propose QoS 1 for telemetry and AI responses. For security, the connection uses MQTT over TLS on port 8883. The ESP32 authenticates to AWS IoT Core with a device certificate and private key, AWS IoT policies restrict it to only the topics it needs, and credentials will never be committed to the public repository. Device-to-cloud topics are greenpulse/sensors and greenpulse/status; the cloud replies on greenpulse/ai/care, ai/weather and ai/notifications." HANDOVER (Member 2 → Member 3): "Once the ESP32 securely publishes the sensor data, the processing moves to our cloud architecture. Member 3 will explain how GreenPulse stores, validates and intelligently processes this information." MEMBER 3 (≈30 sec): "AWS IoT Core delivers the messages to our Python backend, which subscribes, validates each JSON payload and stores timestamped records in DynamoDB, before invoking the LLM and external services. Node-RED subscribes to the same broker to display the results. Because QoS 1 can create duplicates, the backend is designed to de-duplicate using the device ID and sequence number." NOTE: Proposal Figure 1 shows older labels (greenpulse/sensor, greenpulse/llm). Table 5 is authoritative and is what this deck uses.

## Slide 7
07 · CLOUD INTELLIGENCE, LLM & EXTERNAL SERVICES
Turning Measurements into Meaning
Sensor Data
Soil · temp · humidity · light
Weather Data
Real weather API
Notification Context
Authorized account, filtered
Cloud Backend
Validate payload
Store in DynamoDB
Filter & prepare context
Structured
input
LLM Intelligence
Structured prompt via an LLM framework (e.g. LangChain)
Runs in the cloud — not on the ESP32
Care Tip
Literary Quote
Weather Summary
Notification Summary
MQTT
→
Node-RED
Grounded AI Processing
Contextual assistance — not a plant-disease diagnosis system.
Use supplied measurements only
Structured prompts
Validate generated output
Avoid invented sensor values
Avoid unsupported plant-health claims
GreenPulse · IT4030 Internet of Things · Project Proposal
07
Notes: PRESENTER: Member 3 | TARGET: 70 sec | Running total ≈ 6:25 SCRIPT: "This is where GreenPulse goes beyond basic monitoring. The cloud backend combines three inputs: the validated sensor data, current weather from a real weather API such as OpenWeatherMap, and relevant, filtered messages from an authorized email or notification account. The backend validates, stores and prepares this into a structured input with units and timestamps. An LLM — coordinated through a Python framework such as LangChain — then generates four outputs: a care tip, a literary-style quote inspired by the plant's conditions, a weather summary, and a notification summary. These are validated as JSON and published through MQTT to Node-RED. The LLM runs in the cloud, not on the ESP32 — the microcontroller focuses on sensing and communication. Reliability is central. We call it grounded AI processing: the model uses only the supplied measurements, receives structured prompts, and its output is validated. It is instructed not to invent sensor values or make unsupported plant-health claims. GreenPulse provides contextual assistance — it is not a plant-disease diagnosis system." HANDOVER (Member 3 → Member 4): "The final stage is presenting this sensor and intelligent information to the user. Member 4 will explain the Node-RED dashboard and overall system integration." FACTS: Missing/invalid readings are excluded from LLM input. On LLM failure the backend logs the error and applies a predefined recovery procedure. Email: minimum permissions, filtering to plant-care-related messages, raw email never published to MQTT.

## Slide 8
08 · NODE-RED DASHBOARD & USER EXPERIENCE
Everything the User Needs, in One View
GreenPulse
Dashboard
Sensors
AI Insights
Weather
Notifications
MQTT Monitor
Plant Overview
greenpulse_01 · illustrative values
Live
LIVE SENSORS
45 %
Soil Moisture
28.1 °C
Temperature
62 %
Humidity
320 lx
Light
DEVICE
Wi-Fi
Connected
MQTT
Connected
Priority
Normal
AI CARE
Care tip
Monitor the soil moisture before the next watering.
Generated quote
“Every leaf tells a story of the care it receives.”
CONTEXT
Weather Summary of current conditions
Notifications Relevant reminders summarised
SYSTEM
MQTT topic
greenpulse/sensors
Last message
10:30:00 UTC
LLM input
Structured · ready
LLM output
Validated JSON
GreenPulse · IT4030 Internet of Things · Project Proposal
08
Notes: PRESENTER: Member 4 | TARGET: 50 sec | Running total ≈ 7:15 SCRIPT: "The Node-RED dashboard is the single place where the user sees everything. This proposed layout, based on Figure 8 of our proposal, shows live sensor values for soil moisture, temperature, humidity and light; the device's Wi-Fi, MQTT and priority status; the AI care section with the generated tip and quote; the context section with weather and notification summaries; and a system panel showing the MQTT topic, timestamp, and the LLM input and output status. Showing the LLM input next to its output makes the intelligent processing transparent — users can see exactly what data the AI was given." NOTE: All values are illustrative. Node-RED connects securely to the same MQTT broker and subscribes to the telemetry and AI topics. Credentials and unnecessary personal email content are excluded from dashboard payloads.

## Slide 9
09 · IMPLEMENTATION, TESTING & TEAM
Built Incrementally, Tested End-to-End
A · SIX-PHASE INCREMENTAL METHODOLOGY
1 Hardware
2 Firmware
3 Secure MQTT
4 Cloud / LLM
5 Dashboard
6 Integration & Evaluation
B · 15 PLANNED TESTS (T01–T15)
T01–T03
Sensors
Soil · DHT22 · BH1750
T04–T05
Device
OLED · RGB priority
T06–T08
MQTT / Security
TLS · publish · subscribe
T09–T13
Cloud / AI
Backend · DB · LLM · APIs
T14
Dashboard
Payloads · topics · status
T15
End-to-End
Device → cloud → dashboard
C · TEAM RESPONSIBILITIES
1
MEMBER 1
Hardware & Embedded Sensing
ESP32 setup · soil moisture · DHT22 · BH1750 · circuit assembly · GPIO · calibration
Support: Hardware tests & docs · integration testing · demo
2
MEMBER 2
ESP32 Firmware & MQTT
Firmware · acquisition · OLED · RGB priority logic · Wi-Fi · MQTT pub/sub · JSON
Support: MQTT tests · firmware docs · end-to-end testing · demo
3
MEMBER 3
Cloud Backend & Intelligent Processing
Python backend · AWS IoT Core · DynamoDB · validation · LLM · weather · email
Support: Cloud tests · API/security docs · backend integration · demo
4
MEMBER 4
Node-RED, Integration & UI
Dashboard · MQTT visualization · LLM I/O · weather/notification display · integration
Support: End-to-end testing · UI docs · commercial video · demo
GreenPulse · IT4030 Internet of Things · Project Proposal
09
Notes: PRESENTER: Member 4 | TARGET: 60 sec | Running total ≈ 8:15 SCRIPT: "We plan to build GreenPulse incrementally in six phases: hardware, firmware, secure MQTT, cloud and LLM, dashboard, and finally integration and evaluation. Each phase produces a verifiable deliverable before the next begins, which helps us catch problems early. We have planned fifteen tests grouped into six areas — sensors, device outputs, MQTT and security, cloud and AI, the dashboard, and a full end-to-end test from the device to the dashboard. Responsibilities follow the architecture: Member 1 owns hardware and embedded sensing; Member 2 owns ESP32 firmware and MQTT; Member 3 owns the cloud backend and intelligent processing; and I own Node-RED, integration and the user interface. All four of us share integration testing, documentation and the final demonstration." NOTE: Timeline is a proposed four-week plan (Proposal Table 9), prioritising mandatory features before optional extensions.

## Slide 10
10 · EXPECTED OUTCOMES & CONCLUSION
What GreenPulse Is Expected to Deliver
Real-Time Environmental Monitoring
ESP32 sensing with OLED + RGB local status
Secure IoT Communication
Bidirectional MQTT over TLS via AWS IoT Core
Cloud Data Storage
Validated, timestamped records in DynamoDB
Context-Aware LLM Processing
Grounded care tips and literary quotes
Weather & Notification Integration
Real weather API + authorized account
Unified Node-RED Dashboard
Sensors, MQTT info and LLM I/O together
Sensor Data
Context
Intelligence
Better Plant-Care Decisions
GreenPulse · IT4030 Internet of Things · Project Proposal
10
Notes: PRESENTER: Member 4 (or whole group) | TARGET: 40 sec | Running total ≈ 8:55 SCRIPT: "We expect GreenPulse to deliver six outcomes: real-time environmental monitoring, secure IoT communication, cloud data storage, context-aware LLM processing, weather and notification integration, and a unified Node-RED dashboard. In conclusion, GreenPulse proposes an integrated plant-care ecosystem that goes beyond basic sensor monitoring. By combining embedded sensing, secure MQTT communication, cloud processing, external contextual information and LLM-based intelligence, the system aims to transform environmental measurements into meaningful plant-care information through a unified Node-RED dashboard. Sensor data, plus context, plus intelligence — leading to better plant-care decisions. Thank you." LANGUAGE: Keep to "expected", "proposed", "aims to". Do not say "we achieved" or "testing confirmed".

## Slide 11
Thank You
Questions & Answers
GreenPulse — A Healthier Home, A Happier Plant
GreenPulse · IT4030 Internet of Things · Project Proposal
11
Notes: Q&A — 5 minutes. All members stand ready. OWNERSHIP (primary answers first; others may add briefly): • Hardware / sensors / calibration / GPIO → Member 1 • Firmware / OLED / RGB / JSON / MQTT → Member 2 • AWS / DynamoDB / LLM / weather / email / security → Member 3 • Node-RED / dashboard / integration / UI / testing / demo → Member 4 QUICK ANSWERS (proposal-consistent; use "will / proposed"): 1. Problem (M1): Manual checks and fixed schedules miss changes; raw readings are hard to interpret; local sensing lacks context. 2. Innovation (M3/M4): One pipeline joining sensing, secure MQTT, cloud storage, external context (weather + email) and grounded LLM output — with LLM input/output visible on the dashboard. 3. Why ESP32 (M1): Integrated Wi-Fi, GPIO, analog input, digital sensor interfaces (I²C), low cost, supports TLS. 4. Why these sensors (M1): Soil moisture, temperature, humidity and light are the core conditions named in our background; BH1750 gives calibrated lux over I²C. 5. Calibration (M1): Record readings at dry and wet reference conditions and map raw values to a moisture representation; thresholds finalised in prototype testing. 6. MQTT vs HTTP (M2): Lightweight, persistent connection, publish/subscribe decoupling, cloud can push to device (bidirectional), QoS levels. HTTP is request/response and would need polling. 7. Why AWS IoT Core (M3): Managed MQTT broker with TLS, certificate authentication, fine-grained policies, and native AWS integration with DynamoDB (and optionally IoT Rules / Lambda). 8. MQTT over TLS (M2/M3): MQTT carried inside an encrypted TLS session on port 8883; the device validates the server with trusted CA information and authenticates with its certificate + private key. 9. Why JSON (M2): Structured, readable, easy to generate on the ESP32 and parse in Python and Node-RED; allows field validation. 10. Why DynamoDB (M3): Managed AWS storage; device_id partition key + timestamp sort key suits timestamped sensor records; access restricted to required components. 11. Why an LLM (M3): Converts numeric readings plus context into understandable natural-language care information. 12. Why not on the ESP32 (M3): LLMs need far more memory and compute than a microcontroller; the ESP32 focuses on sensing, local status and communication. 13. Reducing hallucinations (M3): Structured input with units; only valid measurements supplied; prompt forbids inventing data; JSON output validation; predefined thresholds add structure. 14. If the LLM is wrong (M3): Output is contextual assistance, not a diagnosis; malformed output is rejected; errors logged and recovery applied; dashboard shows the LLM input for transparency; the RGB priority is rule-based on the device. 15. No AI on OLED (M2): Assignment requirement; the OLED is limited to live readings and MQTT status; AI content belongs to the dashboard layer. 16. RGB LED (M2): Green normal, yellow warning, red critical; critical > warning > normal. 17. Wi-Fi unavailable (M2): Firmware monitors and reconnects; sensing, OLED and RGB are designed to continue locally where practical; OLED shows MQTT disconnected. 18. MQTT disconnects (M2): Reconnection procedures; status reflected on the OLED and status topic; QoS 1 for important messages. 19. Weather API fails (M3): Error handling; unavailable data is never presented as current; LLM is told the data is missing. 20. Why weather (M3): External context — e.g. rainfall or high temperature can be relevant to watering decisions. 21. Why email/notifications (M3): Summarises relevant watering reminders, weather alerts and gardening messages; shows integration of a real external service. 22. Email privacy (M3): Authorized account, minimum permissions, filtering to plant-care-related messages, tokens stored in the backend environment, raw email never published to MQTT or the dashboard. 23. Why Node-RED (M4): Flow-based, native MQTT nodes and dashboard widgets; ideal for showing topics, payloads and LLM input/output. 24. Bidirectional MQTT (M2): ESP32 publishes sensors/status; backend publishes ai/* topics; ESP32 subscribes (receives but does not display AI text); optional command topic. 25. Topics (M2): greenpulse/sensors, /status, /ai/care, /ai/weather, /ai/notifications, and /command if implemented. 26. Testing (M4): 15 planned tests T01–T15 plus six-stage incremental integration (see Backup D). 27. Limitations (M4): Prototype scope; accuracy depends on sensors and calibration; relies on connectivity and external services; LLM output is contextual assistance; no claim of long-term plant-growth improvement. 28. Automatic watering (M1): Not assumed as a core feature unless explicitly finalised; treated as a future extension needing actuators and safety mechanisms. 29. Future work (M4): Multiple plants, data-driven watering prediction, automatic watering, additional sensors, AWS IoT Rules / Lambda automation, plant-specific recommendations. 30. Contributions: Each member states their own area (Backup F).

## Slide 12
APPENDIX
Technical Backup Slides
Hidden during the presentation — open only if a question needs detail.
A Circuit & GPIO Mapping
B MQTT Topic Architecture
C JSON Payload Structure
D Testing Plan T01–T15
E Risk & Mitigation Matrix
F Four-Member Workload Allocation
Notes: Hidden appendix. To jump to a backup slide during Q&A in Slide Show mode, type its slide number and press Enter (e.g. 13 for Backup A), or right-click → See All Slides.

## Slide 13
BACKUP A
Circuit & GPIO Mapping
Preliminary ESP32 GPIO configuration (Proposal Table 2)
Component | Interface | ESP32 Connection
Soil moisture sensor | Analog, if applicable | GPIO34
DHT22 | Digital | GPIO4
BH1750 | I²C SDA / SCL | GPIO21 / GPIO22
OLED display | I²C SDA / SCL | GPIO21 / GPIO22
RGB LED — Red | Digital output | GPIO25
RGB LED — Green | Digital output | GPIO26
RGB LED — Blue | Digital output | GPIO27
Shared I²C bus
BH1750 and OLED share GPIO21 / GPIO22, provided their addresses are compatible.
RGB LED protection
Each colour channel driven through current-limiting resistors.
Power & grounding
Regulated supply, common ground and suitable logic levels.
Build approach
Breadboard first; each sensor tested individually before full assembly.
GreenPulse · IT4030 Internet of Things · Project Proposal
Backup A
Notes: Owner: Member 1. Tip if asked: GPIO34 is an input-only pin on an ADC1 channel, which suits an analog sensor while Wi-Fi is active (ADC2 channels conflict with Wi-Fi on the ESP32). The exact soil-sensor model and interface are confirmed during hardware finalisation.

## Slide 14
BACKUP B
MQTT Topic Architecture
Prefix greenpulse/ followed by message category (Proposal Table 5)
Topic | Publisher | Subscriber | Purpose
greenpulse/sensors | ESP32 | Cloud backend, Node-RED | Environmental sensor measurements
greenpulse/status | ESP32 | Cloud backend, Node-RED | Device and connectivity status
greenpulse/ai/care | Cloud backend | ESP32, Node-RED | LLM care tips and literary quotes
greenpulse/ai/weather | Cloud backend | ESP32, Node-RED | Weather-related summaries
greenpulse/ai/notifications | Cloud backend | ESP32, Node-RED | Relevant email / notification summaries
greenpulse/command | Cloud backend | ESP32 | Device commands / config (if implemented)
MQTT over TLS · port 8883
QoS 1 · at-least-once delivery
Backend de-duplicates via device_id + sequence_number
The ESP32 subscribes to selected cloud topics to demonstrate bidirectional messaging, but never renders AI text on its OLED.
GreenPulse · IT4030 Internet of Things · Project Proposal
Backup B
Notes: Owner: Member 2 (topics, pub/sub) with Member 3 (broker, policies, de-duplication). QoS 1 means at-least-once delivery, so duplicates are possible — hence de-duplication using device_id and sequence_number.

## Slide 15
BACKUP C
JSON Payload Structure
Proposed formats (Proposal Examples 3.1–3.3) — values are illustrative
Sensor telemetry
greenpulse/sensors
{
"device_id": "greenpulse_01",
"sequence_number": 125,
"soil_moisture": 45,
"temperature": 28.1,
"humidity": 62,
"light_intensity": 320
}
Device status
greenpulse/status
{
"device_id": "greenpulse_01",
"firmware_version": "1.0.0",
"priority": "normal",
"wifi_connected": true,
"mqtt_connected": true
}
AI care message
greenpulse/ai/care
{
"device_id": "greenpulse_01",
"timestamp":
"2026-09-17T10:30:00Z",
"priority": "normal",
"care_tip": "Monitor the soil…",
"literary_quote": "Every leaf…"
}
DynamoDB key: device_id (partition) + timestamp (sort), ISO 8601 UTC · backend adds server-side timestamps · payloads validated before storage or LLM use
GreenPulse · IT4030 Internet of Things · Project Proposal
Backup C
Notes: Owner: Member 2 (payload creation) with Member 3 (validation and storage). Values are illustrative, not experimental results. Final telemetry will include any additional sensors retained in the finalised design.

## Slide 16
BACKUP D
Detailed Testing Plan T01–T15
ID | Component | Test procedure | Expected result
T01 | Soil moisture | Readings under dry and wet reference conditions | Values change consistently with conditions
T02 | DHT22 | Read temperature and humidity | Valid temperature and humidity values
T03 | BH1750 | Measure light under different lighting | Readings respond to illumination changes
T04 | OLED display | Update values; change MQTT state | Live readings and MQTT status shown correctly
T05 | RGB LED | Apply normal / warning / critical conditions | Correct priority colour displayed
T06 | Secure MQTT | Connect ESP32 to AWS IoT Core using TLS | Authenticated connection established
T07 | MQTT publishing | Publish sensor telemetry | Valid JSON received on the correct topic
T08 | MQTT subscription | Publish to a subscribed response topic | ESP32 receives it; no AI text on OLED
T09 | Cloud backend | Send valid and invalid payloads | Valid processed; invalid handled
T10 | Data storage | Publish readings; inspect database | Timestamped records stored & retrievable
T11 | LLM processing | Submit structured measurements | Correctly formatted care tip + quote
T12 | Weather API | Request current weather | Real data retrieved or errors handled
T13 | Email integration | Retrieve relevant messages | Summarised without exposing credentials
T14 | Node-RED | Publish sensor and AI messages | Measurements, payloads, topics, status shown
T15 | End-to-end | Run the complete workflow | Device → cloud → MQTT → dashboard works
GreenPulse · IT4030 Internet of Things · Project Proposal
Backup D
Notes: Owner: Member 4 (overall testing) — each member answers for their component's tests. Evaluation focuses on functional operation and end-to-end integration, not on proving long-term plant-growth improvements.

## Slide 17
BACKUP E
Risk & Mitigation Matrix
Risk | Potential impact | Proposed mitigation
Incorrect sensor readings | Unreliable environmental information | Calibrate sensors; validate readings before processing
Incorrect circuit connections | Component malfunction or damage | Verify wiring, voltage levels and power before powering
Wi-Fi disconnection | Interrupted communication | Connection monitoring and reconnection procedures
MQTT authentication failure | Device cannot connect to broker | Verify certificates, policies, endpoint and client settings
Cloud service interruption | Delayed data processing | Error handling and suitable retry mechanisms
LLM output errors | Invalid or unsupported care information | Structured prompts, output validation, no unsupported claims
Weather API failure | Missing external weather information | Detect failures; never present unavailable data as current
Email authentication failure | Notification retrieval unavailable | Supported authentication; handle token / connection errors
Cloud or API cost increase | Budget overrun | Monitor usage; configure service limits
Integration delays | Reduced time for evaluation | Develop incrementally; prioritise mandatory features
GreenPulse · IT4030 Internet of Things · Project Proposal
Backup E
Notes: Owner: whoever owns the risk's component; Member 4 for integration delays.

## Slide 18
BACKUP F
Four-Member Workload Allocation
Consistent with Proposal Table 10 — all members contribute to integration, testing, documentation and the demo
Member | Main area | Main responsibilities | Supporting responsibilities
Member 1 | Hardware & Embedded Sensing | ESP32 setup, soil-moisture sensor, DHT22, BH1750, circuit assembly, GPIO configuration, sensor calibration | Hardware testing, hardware documentation, integration testing, part of final demonstration
Member 2 | ESP32 Firmware & MQTT | ESP32 firmware, sensor data acquisition, OLED, RGB LED, priority logic, Wi-Fi, MQTT publishing/subscribing, JSON payloads | MQTT testing, firmware documentation, end-to-end testing, part of final demonstration
Member 3 | Cloud Backend & Intelligent Processing | Python backend, AWS IoT Core integration, DynamoDB, data validation, LLM processing, weather API, email/notification integration | Cloud testing, API/security documentation, backend integration testing, part of final demonstration
Member 4 | Node-RED, Integration & User Interface | Node-RED dashboard, MQTT visualization, LLM input/output display, weather/notification display, system integration | End-to-end testing, UI documentation, commercial video, final demonstration
GreenPulse · IT4030 Internet of Things · Project Proposal
Backup F
Notes: Each member should be able to describe their own main and supporting responsibilities in one sentence.